## Slide 1
Nuuk, 20-01-2015
Greenland Railway
Baldwin Brown
XYZ 99
Purchase of Container Wagons
LCC Calculation
LCC-Presentation-charts_UIC__2015-01-20
Document title:
<number>
Fictional example

## Slide 2
Purchase of 85 new container flat wagons, each carrying 60’ in total.
Once the operator’s quality gate (filter) has been applied, only the container flat wagons of the two companies A and B remain.
Client: Susan Smith
Responsible for the LCC calculation: Baldwin Brown
Team: Baldwin Brown, Martina Miller
Starts: 10/09/2014
Finishes: 20/01/2015
The Life Cycle Costs of both remaining wagons are to be calculated.
Client: Susan Smith
Starting situation
LCC task
Characteristics
Originator of the LCC calculation, dates
1): Status logic: I = identified, A = Agreed D = Decided, P = Preconditions in place
Status logic 1): I A D P
x
<number>
Fictional example

## Slide 3
In/Out Framework
Not relevant / relevant, but not part of the
calculation
Contained in the calculation
Determined on 01/10/2010
by: Baldwin Brown
Management
Investment
Maintenance: container locking system
Maintenance: replacement of wheelsets
One single Sgns-type container wagon
Maintenance: reprofiling wheelsets
Sgns-type 380 container wagon
Maintenance of other parts of the wagon
Energy consumption while operating
Track access charge
Loading / unloading
Max. speed:
120 km/h
<number>
Fictional example

## Slide 4
Product Breakdown Structure / System Environment
Vehicle
Chassis
Mounted part
Undercarriage
Wheelset
…
...
Container lock
...
<number>
Fictional example

## Slide 5
II. Operation
II.1 Energy
II.2 Staff
II.3 Cleaning
II.4 Making available
II.5 Insurance / Communication
II.5.1 Insurance
II.5.2 Duties
II.5.3 Communication
II.6 Other Costs
II.7 Infrastructure use
II.7.1 Fee charged for
line segments
II.7.2 Fee charged for
stations
II.7.3 Fee charged for
stabling
II.7.4 Specific track
equipment /
construction
II.7.5 Other costs
III. Maintenance
IV. Product Failure
IV.1 Planned
IV.1.1 Product Failure
IV.1.2 Delays
IV.1.3 Malfunction
IV.2 Unplanned
IV.2.1 Product Failure
IV.2.2 Delays
IV.2.3 Malfunction
Purchase 2)
I.1 “One-off” preparation for
each product
I.2 “Recurrent” preparation for
each product
I.3 Investment
I.4 Residual value
I.5 Disassembly /
Decommissioning
I.6 Disposal /
Further utilisation
III.0 “One-off” preparation
III.1 Inspection / Diagnostics
III.2 Preventive maintenance /
servicing
III.3 Preventive maintenance
III.4 Condition-based
maintenance
III.5 Corrective maintenance
III.6 Residual value
III.7 Disposal /
Further utilisation
III.8 Support system for vehicle
concerned
LCC cost blocks used for the calculation
2) For simplicity’s sake, the term “purchase” also comprises residual costs as well as disposal / further utilisation.
<number>
Fictional example

## Slide 6
Purpose & brief description of each option
Basic option
Company A
Purpose
Purchase of a 60‘ container wagon with reduced maintenance expenditure.
Alternative option
Company B
Purchase of a 60‘ container wagon with well-known characteristics.
Brief description
Compared to the existing wagon type, both the lifetime of the wheels and the reprofiling cycle are extended. The reliability of container lockings will be significantly improved.
The lower investment cost may result in maintenance expenditure being the same as today.
<number>
Fictional example

## Slide 7
Variants: list of principal differences
Interest rate: 10% (constant)
Inflation rate: 3% (constant)
Life span of wagon: 25 years
Annual mileage: 115,000 km
Earnings are fixed and equivalent for both options. For this reason only the cost structure of the two options will be compared.
Remarks concerning general assumptions for all options, comments and critical factors.
Parameter
Basic option
Company A
Number of wheelsets
4
Alternative option
Company B
4
Type of running gear
Bogie with two radially-adjustable wheelsets
Bogie with two non radially-adjustable wheelsets
Type of container lock
“Advanced” type
“Standard” type
Number of container locks per wagon
20
20
<number>
Fictional example

## Slide 8: Composition of Cost and Cycle Data
Cost Block
Basic option
Company A
Purchase
Alternative option
Company B
65,000 €
one-off
manufacturer
analysis
69,500 €
one-off
manufacturer
analysis
Preventive maintenance: replacing wheel
620 € per wheel
every 750,000 km
operator
analysis
620 € per wheel
every 920,000 km
operator
expert survey
Preventive maintenance: replacing container locks
150 € per container lock
every 185,000 km
operator
analysis
180 € per container lock
every 290,000 km
manufacturer
expert survey
Corrective maintenance:
reprofiling wheelset
200 € per wheelset
every 250,000 km
operator
analysis
200 € per wheelset
every 275,000 km
operator
estimation
Euro
Cycle
Source
Robustness
Euro
Cycle
Source
Robustness
Euro
Cycle
Source
Robustness
Euro
Cycle
Source
Robustness
<number>
Fictional example
Notes: Daten erheben
Wozu:
Für einige Fragestellungen wird die Datengrundlage nicht den Anforderungen entsprechen. In diesem Fall muss eine Datenerhebung angestoßen werden. Dies kann erhebliche Auswirkungen auf den Zeitbedarf für den Gesamtprozess haben.
Wie:
Datenblätter zur Erhebung des korrektiven und präventiven Instandhaltungsaufwands im Rahmen von Ausschreibungen dem Hersteller übermitteln („060411_Datenblätter_LCC_DBAG.xls “).
Formulare (selbst erstellt) zur Datenerfassung aufstellen und vor Ort auf ihre Praktikabilität überprüfen.
Datenerhebung anstoßen bzw. durchführen.
Daten und Ergebnisse aus der Vergangenheit sind genau auf Ihre Übertrag- bzw. Verwendbarkeit zu überprüfen. Dies gilt insbesondere deshalb, da es sich bei fast allen LCC-Aussagen um Vergleichsbetrachtungen handelt.
Daten analysieren
Wozu:
Den richtigen Zeithorizont für die Identifikation der Auswirkungen festlegen.
Wie:
Existierende Datensysteme und Aufzeichnungen erfragen
Daten auf Vollständigkeit und Qualität analysieren
Datensysteme auf Verifikationstauglichkeit analysieren
Kenntnis über die Brauchbarkeit der Daten für die Analyse und die Vertragsverifikation
Z. B. ISI(SAP)-Daten betrachten, Aufzeichnungen der Werke abfragen etc
Zuordnung der Tätigkeitsbezeichnungen / Materialbezeichnungen zu den Kostenblöcken. (Zuordnungsmatrix noch nicht überall vorhanden)
Zuverlässigkeiten feststellen
Auswertung der verfügbaren Datenlage und Expertenwissen (z. B. System- und Modulbetreuer) zur Festlegung der Nutzungsdauer. (Differenzen zwischen technischer Lebensdauer und kaufmännische Nutzungsdauer sind zu beachten)
Hinweis:
Für die Unterstützung bei der Erhebung und Analyse von Daten können die OEen TZF 11, TZF 62 etc. kontaktiert werden.

## Slide 9: Table of values and net present value of variant A
<number>
Fictional example
Notes: Zahlungsreihe ausfüllen
Wozu:
Bestimmung des jeweiligen LCC-Wertes (Barwertes bzw. Kapitalwert) für alle Varianten.
Wie:
Je Variante werden die Jahreswerte je Kostenblock (Zeile) (z. B. aus der Nebenrechnung) in die Zahlungsreihe eintragen.
Dazu sind die ermittelten Häufigkeiten (z. B. auf Basis von Zuverlässigkeiten) je Leistungseinheit mit den ermittelten Kosten oder vorhandenen Standardwerten zu multiplizieren und auf die Jahresscheibe umzurechnen.
Hierzu werden in den meisten Fällen Nebenrechnungen notwendig sein, die auch zur Dokumentation dienen können (siehe „Nebenrechnung durchführen“).
Diskontierung und Teuerung sind gemäß Konzernvorgabe zu berücksichtigen und bereits im LCC-Taschenrechner hinterlegt.
Weitere Hilfestellungen sind in der Excel-Datei LCC-Taschenrechner auf dem entsprechenden Reiter zu finden.

## Slide 10: Table of values and net present value of variant B
<number>
Fictional example

## Slide 11: Overview of results and comments
Other essential aspects.
Aspects intentionally left out of the analysis, the impact of which is as follows: (…)
Comments
Basic option
Company A
Annuity 5)
- 10,317 €
Alternative option
Company B
- 10,585 €
Net present value 3)
- 93,644 €
- 96,079 €
Break-even 4) [years]
13 years
positive value: revenue, negative values: costs
break-even: number of years until the alternative option becomes advantageous
annuity: average annual costs
<number>
Fictional example

## Slide 12: Key Performance Indicators
Responsible Department
Maintenance documentation system
Data Origin
Variation [%]
alternative option to basic option
BCD 31
-
-
-
-
Key Performance Indicator
Mileage between reprofiling wheels
-
-
…
Comments
+ 10 %
+ / - %
+ / - %
<number>
Fictional example

## Slide 13
Profit-and-loss chart (Delta of variant “B” in relation to variant “A” [= zero line])
<number>
Fictional example

## Slide 14
Break-even chart
<number>
Fictional example

## Slide 15
Recommendation
It is recommended to purchase the container wagon made by company B.
Selected Option / Recommendation
Because of the radial adjustability of the wheelsets, the wear rate of the wheels is lower and the lifetime of the wheels and the reprofiling cycle are therefore considerably longer.
Due to the higher quality of the container locks, maintenance expenditure is lower compared with the container wagon made by company A.
Explanatory Statement
Break-even: 13 years
Average Annual Savings (Delta Annuity):
270 € per wagon
Clarify financial options.
Precondition for Implementation
Establish a purchase time schedule.
Obtain approval from financial controlling.
Further Procedure Target Date / Responsibilities
<number>
Fictional example

## Slide 16: Approval status
Compiled by:
Traceability of implementation:
XYZ 99
Baldwin Brown
10/01/2015
Department of Rail Technology
Department
Name
Date
-
Department
Name
Date
-
Validated by client:
BCD 2
Susan Smith
20/01/2015
Rail Operator
Department
Name
Date
Rail Operator
*
Department
Name
Date
Department of Rail Technology
*
* appointet by the Client
<number>
Fictional example